## Slide 1
Computer Arch. a Quantitative Approach 5th Edition
Chapter 1
Fundamentals of Quantitative Design and Analysis
Phillip Kamau
SCT212-0048/2021

## Slide 2: 1.1 Introduction
Performance improvements:
    Improvements in semiconductor technology
        Feature size, clock speed
    Improvements in computer architectures
        Enabled by High Level Language compilers, UNIX
        It lead to RISC architectures
    Together they have enabled:
        Lightweight computers
        Productivity-based managed/interpreted programming languages

## Slide 3: Single Processor Performance
RISC
Move to multi-processor

## Slide 4: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
    Single processor performance improvement ended in 2003
New models for performance:
    Data-level parallelism (DLP)
    Thread-level parallelism (TLP)
    Request-level parallelism (RLP)
These require explicit restructuring of the application

## Slide 5: 1.2 Classes of Computers
Personal Mobile Device (PMD)- emphasis is on energy efficiency and real-time. e.g smart phones, tablet computers
Desktop computing- emphasis is on price-performance
Servers- emphasis is on availability, scalability and throughput
Clusters/ Warehouse Scale Computers-
  used for SaaS
  emphasis is on availability and price-performance
  Sub-class: supercomputers, emphasis: floating-point performance and fast internal networks
5. Embedded Computers - emphasis is on price
Feature | Personal mobile device (PMD) | Desktop | Server | Clusters/warehouse-scale computer | Embedded
Price of system | $100–$1000 | $300–$2500 | $5000–$10,000,000 | $100,000–$200,000,000 | $10–$100,000
Price of micro-Processor | $10–$100 | $50–$500 | $200–$2000 | $50–$250 | $0.01–$100
Critical System Design Issues | Cost, energy, media performance, Responsiveness | Price- performance, energy, graphics Performance | Throughput, availability, scalability, energy | Price-performance, throughput, energy Proportionality | Price, energy, application specific Performance

## Slide 6: Parallelism
Classes of parallelism in applications
    Data-Level Parallelism (DLP)
    Tak-Level Parallelism (TLP)
Classes of architectural parallelism
    Instruction-Level Parallelism (ILP)
    Vector architectures/Graphical Processor Units (GPUs)
    Thread-Level Parallelism
    Request-Level Parallelism

## Slide 7: Flynn’s Taxonomy
Single instruction stream, single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
    vector architectures
    Multimedia extensions
    Graphics processor units
Multiple instruction streams, single data stream (MISD)
    No commercial implementation
Multiple instruction streams, multiple data streams (MIMD)
    Tightly-coupled MIMD
    Loosely-coupled MIMD

## Slide 8: 1.3 Defining Computer Architecture
“Old” view of computer architecture:
    Instruction Set Architecture (ISA) design
    i.e. decisions regarding:
      registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
“Real” Computer architecture
    specific requirements of the target machine
    Design to maximize performance within constraints: cost, power and availability
    Includes ISA, microarchitecture, hardware

## Slide 9: Organization, Hardware and Architecture
Organization: includes the high-level aspects of a computer’s design
    memory system, the memory interconnect and the design of the internal processor or CPU (architecture, logic, branching and data transfer).
    E.g. AMD Opteron 64 and Intel P4 have same ISA but they have different internal pipeline and cache organizations.
Hardware: detailed logic design and the packaging technology.
    E.g. P4 and mobile P4 have the same ISA and organization, but they have different clock frequency and memory system.
Architecture: covers all three aspects of computer design - instruction set architecture, organization and hardware.
    Designer must meet functional requirements as well as price, power, performance and availability goals.

## Slide 10: 1.4 Trends in Technology
A successful new ISA may last decades, for example, IBM mainframe.
There are four critical technologies:
    Integrated circuit logic technology- transistor density increased by about 35% per year quadrupling in somewhat over four years
    Semiconductor DRAM(Dynamic Randon-Access Memory)- capacity increases by about 40% per year doubling roughly every two years.
    Magnetic disk technology- roller coaster of rates, disk are 50-100 times cheaper per bit than DRAM.
    Network technology- network performance depends both on the performance of switches and transmission.

## Slide 11: Performance Trends: Bandwidth over latency
Bandwith or throughput: the total amount of work done in a given time.
      such as megabyte per second for a disk transfer
Latency or response time: the time between the start and the completion of an event
      Such as milliseconds for a disk access

## Slide 12: Scaling of Transistor Performance and wires
Feature size- the minimum size of a transistor or a wire in either the x or y dimension.
    From 10 microns in 1971 to 0.32 microns in 2011.
    The density of transistors increases quadratically with a linear decrease in feature size.
    Transistor performance improves linearly with decreasing feature size
    Since improvement in transistor density, thus CPU move quickly from 4-bit to 8-bit to 16-bit to 32-bit microprocessors.
    Signal delay for a wire increases in proportion to the production of its resistance and capacitance.

## Slide 13: 1.5 Trends in Power in Integrated Circuits
Power also provides challenges as devices are scaled.
  Dynamic power (watts, W) in CMOS chip - the traditional dominant energy consumption has been in switching transistors.
    Powerdynamic = 1 ⁄ 2 x Capacitive load x Voltage2 x Frequency switched
    In modern VLSI, the exact power measurement is the sum of:
      Powertotal = Powerdynamic + Powerstatic + powerleakage
  For mobile devices they care about battery life more than power so energy is the proper metric, measured in joules:
      Energydynamic = Capacitative load x Voltage2
  Hence lower voltage can reduce Powerdynamic and Energydynamic greatly. (In the past 20 years, supply voltage is from 5V down to 1V)

## Slide 14
As we move from one process to the next (60nm or 45nm ...)
    Transistor switching and frequency ;
    Capacitance and voltage ;
    However, power consumption and energy .
Static power- an important issue because leakage current flows even when a transistor is off:
Powerstatic = Currentstatic x voltage
    Thus, transistor , power ;
    Feature size , power .

## Slide 15: 1.6 Trends in cost
Cost driven down by learning curve
    Yield
DRAM- price closely tracks cost
Microprocessors- price depends on volume
    10% less for each doubling of volume

## Slide 16: Cost of an Integrated Circuit (IC)
Bose-Einstein formula:
Today’s technology: